## Slide 1
Vehicle Accident Prevention System
Associate professor. Sanaa Taha,
Manger of Information Technology Program
Egyptian E-Learning University
Eng. Mohamed Hassan Omar,
Teaching Assistant at faculty of Computer and
Information Technology Egyptian E-Learning University
EELU - Information Technology
2020-2021

## Slide 2
Contents
Title | 01
Introduction | 03
Statistics | 04
Problem Solution | 05
Components and Material Required | 10
Implementation | 11
Architecture flowchart | 22
Prototype | 24

## Slide 3: Introduction
The Central Agency for Public Mobilization and Statistics (CAPMAS) announced that car accidents in Egypt rose by 17.8 percent in 2019, compared to 2018 [1]. These accidents have many causes such as Distracted, Speeding, alcoholic and Reckless Driving , etc… The common factor for all these reasons is the lose of both optical and auditory effect, so we aim to design a system that can warn the driver optically and Acoustically to gain attention and try not to have a collision with the front vehicle. The system are divided into hardware part that consist of Arduino Uno, Peizo buzzer, led lights, raspberry pi, and Laser Reader and software part which is a machine learning model that classify and express the level of danger to make best action to prevent collision with the front vehicle.

## Slide 4: Statistics
Chart: The number of accidents of cars that occurred on the roads in the provinces and highways
| 2014 | 2015 | 2016 | 2017 | 2018 | 2019
Series 1 | 6500 | 6916 | 7101 | 5836 | 4426 | 5220
Column2
Column1

## Slide 5
According to researches human tends to focus with both the auditory and optical senses so to grab driver attention and alert him with the road dangers and potential risk we design a system that contain audible and optical alarms to arouse driver and try to avoid collision. If the driver doesn't respond to these elements so in this case before any thing harm take place there will be an alternative automatic respond by automatically stop the car through breaks by measuring distance between the objects (cars) and the speed of the car then determine which action to take according to zone which the car in. Our solution are Based on hardware part that take measurements of inputs and send to software part which is a machine learning model that classify level of danger based on measurements and respond with class of danger by which hardware part make an alarm or in such cases make physical respond.
Problem Solution

## Slide 6
if distance is greater than 70 units and speed confined between 80-110 units the No warning.
Distance between vehicles and Speed of car segmented into four different zones:
Problem Solution
Zone A
Zone B
Zone C
Zone D

## Slide 7
Distance between vehicles and Speed of car segmented into four different zones:
Problem Solution
Zone A
Zone C
Zone D
Zone B
if distance confined between 50-70units and speed confined between 80-110 units then Only visual warning blue LED will glow to alert
(In this zone driver has to pay attention).

## Slide 8
Distance between vehicles and Speed of car segmented into four different zones:
Problem Solution
Zone A
Zone B
Zone D
Zone C
if distance confined between 35-50 units and
speed confined between 40-80 units then
visual warning red LED will glow to alert and Buzzer will start at low frequency and slow
down (In this zone driver has to pay attention).

## Slide 9
Distance between vehicles and Speed of car segmented into four different zones:
Problem Solution
Zone A
Zone C
Zone B
Zone D
if distance is less than 35 units and speed less than 40 units then Both visual and audio warning red LED glow to alert and Buzzer will start at high frequency and break ( Driver has to take necessary action to avoid collision).

## Slide 10: Components and Material Required Arduino Car Raspberry pi Piezo Buzzer TF Mini LiDAR LED

## Slide 11: Implementation
First phase
Second phase
Is the Arduino code for your information method of transferring result is used trough Bi directional serial communication between Arduino and raspberry pi using the UART protocol. Moreover, the Arduino take the proper action by initiate an alarm (Visual and auditory). Next part will explain two phases in details.
Is machine learning model that are loaded in Raspberry pi that can predict and classify danger based in inputs that is given to inputs are(speed , average speed ,distance and moved).After model classify level of danger which can be level A or B or C or D it transfers result to the Arduino.
Software implementation consist of two
phases

## Slide 12: Implementation
Following steps demonstrate previous phases:
This code is implemented on Arduino IDE which measure distance by TF-mini.
Step 1

## Slide 13: Implementation
Check Bi directional serial communication between Arduino and Raspberry pi using the UART protocol
Step 2
Arduino communication code:

## Slide 14: Implementation
Raspberry pi communication code:

## Slide 15: Implementation
Machine learning model that are loaded in Raspberry pi that can predict and classify danger based in inputs that is given
Step 3
Before we build our model we search for Appropriate dataset which help us to build good Model.
Then we used dataset that were provided by (Zenodo) and contain variables and records of data.
After this Step we have determined the number of classes ( Zone ) to implement it by our model.

## Slide 16: Implementation
Samples of dataset

## Slide 17: Implementation
Next part choosing the most suitable algorithm that achieve high efficiency so we select many algorithms and test them to select the accurate one, the selected as follows:
Naive Bayes With accuracy = 92%

## Slide 18: Implementation
Logistic Regression With accuracy = 97%

## Slide 19: Implementation
K-Nearest Neighbors With accuracy = 99%
Therefore, according to the previous KNN achieved the highest accuracy we use it in implementation.

## Slide 20
Next part based on accuracy of KNN, we try to test model
load KNN model from disk
predict function to return the right zone
Implementation

## Slide 21
call function to test the model and print the result
samples of testing output
Implementation

## Slide 22
Architecture flowchart
Start
TF measure
Model classify
Class A
Class B
Class C
Class D
No Alarm
(Zone A)
Blue LED Alarm
(Zone B)
Slow Down,
Red LED Alarm, low Buzzer
(Zone C)
Red LED
Alarm, High
Buzzer , Break
(Zone D)
yes
yes
yes
yes
No
No
No
No

## Slide 23
Distance between vehicles and Speed of car segmented into four different zones:
Implementation

## Slide 24
Prototype

## Slide 25
Prototype

## Slide 26: Thanks